## Slide 1: 光、毫米波通信集成电路与初创企业
Prof. C. Patrick Yue 俞捷, 香港科技大学
首届“湘智兴湘”大会 — 湖南 长沙
2025-09-19
Hi5 Semiconductor
High5 Semiconductor (Hong Kong) Limited
高武半導體(香港)有限公司
Integrated Circuit Design Center, Optical Wireless Lab
Department of Electronic and Computer Engineering
The Hong Kong University of Science and Technology (HKUST)
High5 Semiconductor (HK) Limited 高武半導體(香港)有限公司

## Slide 2: 内容綱要
團隊成員與技術協同
市場機遇
技術路綫與目標市場
產品描述與原型
商務拓展

## Slide 3: CMOS芯粒+GaN芯粒領域的綜合技術專長
CMOS + GaN = High-End Eco-Semiconductor Chiplets
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
“High-SPLIQ”
High-Speed
High-Power Efficiency
High-Linearity
High-Integration
High-Q-Factor Passives
Deep partnership GaN foundry Dynax
Process development and device optimization
Our CGTA Prof. Man Hoi Wong is an expert in wide-bandgap semiconductors
Co-founder of Atheros, IPO in 2004
Developed First-gen Wifi products
Fellow, IEEE & Optica
HKUST IC Design Center Director
Expert in CMOS optical and wireless communication IC
Prof. C. Patrick Yue
Heterogenous integrated system-in-package (HISiP)
Partnering with Faraconix on RF module integration
Jointly tackling heat and high-freq loss issues
Dr. Chi Law
High-Energy Efficiency

## Slide 4: High5 Semi 的解決方案 / 深度技術 / IP
透過異質集成芯粒封裝技術 Heterogeneous Integration of Chiplets 同時解決無線與光通信技術瓶頸，並滿足降低成本的產業需求
By integrating CMOS + GaN we aim to deliver best-in-class energy-efficient solutions for the two highest growth enterprise communication market in the next decade:
  High-speed optical communication for Data Center Interconnection (DCI)
  Satellite communication for 6G networks
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.

## Slide 5: 内容綱要
團隊成員與技術協同
市場機遇
技術路綫與目標市場
產品描述與原型
商務拓展

## Slide 6: 市場機遇 & 總潛在市場 (TAM) 預測
光通信市場規模：
中國與全球其他地區 (單位：USD Million)
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
Sales ($B)
全球衛星通信市場規模：
按軌道類型劃分 (單位：USD Billion)
For the first stage, optical communication products for DCI, the total addressable market in next 5 years is 40 billion USD
For the second stage, wireless communication products for LEO satellite communication, the total addressable market in next 5 years is 26 billion USD

## Slide 7: 數據中心光通信模塊市場機遇
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
數據中心互連光模塊
新一代數據中心互連需要高效率、高速的光收發模塊

## Slide 8: 數據中心光通信模塊市場機遇
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
Interconnect Power and Density Bottleneck
Internal chips are slow, but >50Tb interface to ICs overwhelm packaging density
200Gb/s SERDES take area, yield, and power, all with limited reach

## Slide 9: 數據中心光通信模塊產品挑戰
Current optical communication products (InP, SiGe, GaAs) cannot meet high-energy efficient bandwidth and cost requirements
Low-frequency solutions fail for modern data center interconnects
Due to the data exchange and transmission requirements brought by AIGC, the market for high-speed optical modules have seen exponential growth
Designing heterogeneous optical chiplets to boost bandwidth and data rates
Targeting 4x bandwidth growth from 200/400G to 1.6T optical modules
AIGC數據中心互連遇到的帶寬瓶頸
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
拒绝被卡脖子!​​
Refused to be choked!

## Slide 10: 6G衛星通信市場機遇
6G及未來衛星通信的全球競賽：
有限的頻譜資源與傳輸容量
LEO capacity limit: < 100K satellites
China's opportunity: Must develop a Starlink-level solution to ensure global competitiveness in satellite internet
ITU rules: "First come, first served", escalating the race
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
5 million customers in 2025 for revenue US$3B
Notes: LEO can safely accommodate only 60,000 to 100,000 satellites
Intense global competition for these limited orbital and frequency resources
The International Telecommunications Union (ITU) operates on a "first come, first served" basis, escalating the race
Current CMOS-based transceivers and digital processing solutions lack the needed output power for LEO communication: 10,000x short of requirements

## Slide 11: 6G衛星通信產品挑戰
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
Long-distance inter-satellite communication requires high-end eco-semiconductors
  High-integration CMOS circuit array
  High-energy-efficiency GaN power amplifiers
  Heterogeneous chiplet packaging technology
CMOS phased array circuits: 10~20x power enhancement
GaN technology: 10~50x power boost with high-voltage operation
Overall 1,000x Power Increase!
Unprecedent Performance in Integration/Power/Efficiency/Cost!
Mechanical satellite tracking
Electrical and digital beamforming
Combining individual PAs and LNAs for gain enhancement
當前市場領導者 : StarLink Satcom

## Slide 12: 内容綱要
團隊成員與技術協同
市場機遇
技術路綫與目標市場
產品描述與原型
商務拓展

## Slide 13: High5 CMOS+GaN 無線與光通信技術路線圖概覽
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
Stage | Key Deliverables
RAISe+ Stage 1 R&D focusing on optical chiplet module (Year 1~3, 2026~28) | Performance analysis of (CMOS+GaN) materials
 | Initial design and prototype of (CMOS+GaN) HiSiP for data center interconnection
 | Prototype for short-reach 1-2 Tb/s links
RAISe+ Stage 2 Commercialization (Year 4~5, 2029~30) | Mass production of optical communication products
 | Design (CMOS+GaN) chiplets for 6G satellite communication
 | Compliance with 3GPP Release 18 and Chinese satellite standards

## Slide 14: 内容綱要
團隊成員與技術協同
市場機遇
技術路綫與目標市場
產品描述與原型
商務拓展

## Slide 15: 產品描述: CMOS + GaN Chiplet HiSiP
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
數據中心互聯的光通信異質集成芯粒
衛星通信的無線異質集成芯粒
Cross section of the wireless chiplet in a package
3D Layout of the wireless chiplet in a package
Integrated optical module (source: Marvell)
Cross section of the optical chiplet in package

## Slide 16
CMOS 產品原型：48-Gb/s PAM-4 Optical Receiver
C. Zhang, C.P. Yue et al., VLSI 2024, Honolulu, HI, USA.
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
16
Fabricated in 28-nm bulk CMOS
1308-nm light source is coupled to PD through a single-mode fiber
Optical power level is adjusted by an internal optical attenuator
Deserialized MSB and LSB are sent to off-chip BER testing

## Slide 17
CMOS 產品原型：56-Gb/s PAM-4 Optical Transmitter
F. Chen and C. P. Yue, ESSCIRC 2023, Lisbon, Portugal.
Data path: thermometer-coded architecture
Clock path: Wideband PLL and cascading VCDL
Optical part: Wire-bonded anode-driven VCSEL
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
17

## Slide 18
CMOS 產品原型：60-Gb/s CDR with Jitter Compensation
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
18
The receiver integrates a Clock and Data Recovery (CDR), capable of detecting the phase and amplitude of the input jitter and generating a complementary jitter to negate the jitter transfer.
Prototyped in 40nm CMOS
Core area: 0.2 mm2
30-60-Gb/s PAM-4 Receiver with Jitter Compensation CDR System Diagram
Complementary Signal Generator
L. Wang, Z. Zhang, C. Wang, R. Azmat, W. Shi and C. P. Yue, "A 60-Gb/s 1.2-pJ/bit 1/4-Rate PAM-4 Receiver With a Jitter Compensation CDR," in IEEE Journal of Solid-State Circuits, vol. 59, no. 2, pp. 449-463, Feb. 2024
60-Gbps PAM-4 Receiver with Jitter Compensation CDR

## Slide 19
CMOS 產品原型：28GHz Phased-array Beamformer
Beamsteering Demo
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
19

## Slide 20
CMOS 產品原型：20–24-GHz Sub-Sampling PLL
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
20
A low-noise charge-domain gain control technique provides a bandwidth tuning range greater than 30 dB, with noise contribution less than 3 fs
The design achieves a compact area (0.057 mm²) and ultra-low jitter (61.23 fs), making it highly suitable for integration into phased array systems
L. Wang, Z. Liu, R. Ma and C. P. Yue, "A Compact 20–24-GHz Sub-Sampling PLL With Charge-Domain Bandwidth Control Scheme," in IEEE Journal of Solid-State Circuits, vol. 60, no. 3, pp. 768-784, March 2025
22-GHz Compact, Low-Jitter Dual-path Sub-Sampling Phase-Locked Loop
Total Chip Area: 0.126 mm2
Core Area: 0.057 mm2
System architecture of the proposed DPSSPLL

## Slide 21
GaN 產品原型: PA, LNA, Laser Diode Driver
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
21
Fig. a
Fig. b
Top-view of a GaN low-noise Amplifier (LNA) chip with bumps
Top-left view of a GaN power amplifier (PA) chip with bumps
Top-view of a GaN laser diode driver (LDD) chip with bumps
Copper Pillar Bumps for Flip-chip Bonding
Fig. c

## Slide 22
先進封裝產品原型：Chip-to-antenna-on-PCB Design
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
22
Antenna array
  4 flipped patches, 4 dummy patches
  Flipped patch driven by differential signals
  Dummy patches are ground
Z. Liu, L. Wang, R. Ma, Z. Chen and C. Patrick Yue, "A Compact 28-GHz Transmitter Front End With Co-Optimized Wideband Chip–Antenna Interface," in IEEE Transactions on Microwave Theory and Techniques
  Photo of the top side (chip) and back side (antenna)
  EM model of patch antenna on PCB

## Slide 23
先進封裝產品原型: Interposer Substrate Design
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
9/28/2025
23
PCB
HEMT
PA
CMOS TRx
Double-sided flip-chip-bonding
Passive components in the middle layer of the interposer for matching, filtering, etc.
Front-end modules on the top side
CMOS chiplets on the back side
Solder balls to connect the interposer to the PCB
Patch antennas will be designed on PCB
Dual-side Interposer for Wireless Satcom
  Dual-side Co-Packaged Optics (CPO)
Double-sided flip-chip-bonding
Direct Multi-Core Fiber (MCF) buttom-coupling
Core-less organic build-up interposer (thinner)

## Slide 24: 内容綱要
團隊成員與技術協同
市場機遇
技術路綫與目標市場
產品描述與原型
商務拓展

## Slide 25: 產品競爭力 / 市場格局
Competitive Analysis | Area | Company | Product Descriptions
Optical Communication Products for DCI | Domestic |  | 100G/400G/800G optical modules, optoelectronic chips, lasers, etc.
 | Global |  | High-speed optical modules (400G/800G), optoelectronic chips (CPO), PAM4 chips, high-speed DSP chips
Wireless Products for Satellite Communication | Domestic |  | Satellite ground equipment, inter-satellite communication modules, RF front-end chips, low-earth orbit satellite terminals
 | Global |  | Satellite communication terminals, low-earth orbit satellite networking systems, RF front-end modules, high-speed ADC/DAC chips
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.

## Slide 26: 與 RAISe+ 相關的合作夥伴及背書支持
Packaging Partner
Investors and Customers
Other Partners
GaN Partner
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
6 technology R&D partners
4 engaged customers

## Slide 27: 與 GaN 行業建立戰略合作夥伴關係
與 GaN 代工夥伴 Dynax (蘇州能訊高能半導體)
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
與 GaN & micro-LED 代工夥伴 Sitan (思坦科技）

## Slide 28: 總部設立於香港科學園（HKSTP）
在香港註冊並設立辦公室
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
由香港投資推廣署（InvestHK）支持

## Slide 29: 傳媒廣汎關注與報道
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2025.
獲批港府創新科技署(ITC)產學研1+(RAISe+)資助，受到傳媒廣汎關注
信報
HKEJ
香港電臺
RTHK
大公報
明報
星島日報
華僑報

## Slide 30: Acknowledgements (HKUST OWL🦉Alumni)

## Slide 31: Acknowledgements (HKUST OWL🦉Current Members)

## Slide 32: Thanks! 謝謝!
high5semi@gmail.com
https://high5semi.github.io/
High5 Semiconductor (HK) Limited 高武半導體(香港)有限公司
Optical Wireless Lab
Department of Electronic and Computer Engineering
The Hong Kong University of Science and Technology (HKUST)
Hi5 Semi
High5 Semiconductor (Hong Kong) Limited
高武半導體(香港)有限公司