## Slide 1
Optical, Wireless, and Optical Wireless Communication and a Brave Startup
光、无线、及光无线通信，和一个勇敢的初创公司
C. Patrick Yue 俞捷 Hong Kong University of Science and Technology
OWL ICDC ECE

## Slide 2: Outline
Optical, Wireless, and Optical Wireless – What? Why?
Optical-Electronic Integrated Circuit (OEIC)
CMOS mmWave Phased-Array IC
High-SPLIQ IC for 6G Era
New Potential Applications in the 6G Era
Summary

## Slide 3: Optical, Wireless, and Optical Wireless
Copper: high loss, low bandwidth
Fibers: low loss, high bandwidth, need OE-EO
Optical for Distance X Data Rate > 100 Gb/s-m
Cross-over opportunities!!
High-Speed OWC, Short-Reach Optical

## Slide 4
Ethernet Wireline Link
Non-terrestrial networks (NTN)
(Source: Texas Instruments,2022)
High-SPLIQ IC and SiP required in advanced enterprise communication applications
Optical fiber network for 5G network back-, mid-, front-haul connectivity

## Slide 5
Optical-Electronic Integrated Circuit (OEIC)

## Slide 6
CMOS Optoelectronic Interconnect Chip: Architecture Design
56-Gb/s PAM4 TX
Data path implements VCSEL nonlinearity compensation
Clock path has on-chip PLL
Fully-Integrated System Architecture Design and Verification
Top-down system simulation to clarify specifications for each module
Multi-chip system simulation throughout the entire design cycle
Support complex modulation scheme, like PAM-4, OFDM, QAM
56-Gb/s PAM4 RX
Signal equalization in frequency domain
PAM4 signal decoding and clock recovery
14-GHz PLL
Sub-sampling PLL achieves low jitter
Low supply voltage to decrease power
PAM4 Optoelectronic Interconnect Chip EMI Analysis and Cancellation
Clarify radiation theory of CM noise
Propose close-loop controlling of CM noise
Propose CM noise cancellation circuit

## Slide 7
课题负责人：俞捷
课题汇报单位：香港科技大学
参与单位：
华南理工大学、南方科技大学
2024. 01. 22

## Slide 8
项 目 分 工
PAM4光电互联芯片整体设计
研究内容
项目实施
俞捷教授
余浩教授
潘权教授
陈志坚高工
PAM4光电互联芯片接收器前端设计
PAM4光电互联芯片发射端信号失真补偿
统筹项目工作计划和进度总体控制。负责组织课题工作的汇报、检查和验收
协助承担单位完成项目立项、中期审查、项目结题等工作
香港科技大学
华南理工大学
南方科技大学
PAM4光电互联芯片整体设计

## Slide 9
High-linearity 56-Gb/s PAM4 TX chip
Based on 4-to-1 MUX, including data path, clock path, and bias and control part
Data path: adopting thermometer code-based architecture for piecewise compensating E/O gain and bandwidth nonlinearities
Clock path: multi-phase PLL to generate 8-phase clock
On-chip PRBS for testing
8

## Slide 10
High-linearity 56-Gb/s PAM4 TX chip：4-2-1 MUX design
Implemented in 40nm CMOS，0.1 mm2 of core area
Tuned slice EQ and slice gain to compensate for the VCSEL nonlinearity

## Slide 11
 | PTL’18 | JSSC’22 | VLSI’19 | ASSCC’21 | This work
Technology [nm] | 65 | 40 | 65 | 40 | 40
Signalling scheme | 1/2-rate PAM-4 | 1/4-rate PAM-4 | 1/4-rate PAM-4 | 1/4-rate PAM-4 | 1/4-rate PAM-4
Date rate [Gbps] | 50 | 56 | 64 | 64 | 56
OMA [mW] | 2.00 | 0.81 | 2.50 | 1.08 | 1.18
Power effi. [pJ/b] | 5.12 | 1.73 | 2.69 | 2.09 | 2.05
Core area [mm2] | 0.31 | 0.47 | 0.28 | 0.16 | 0.10
Asymmetric equalization | 2.5-tap DAC-based FFE | 2-tap DAC-based FFE | 3-tap LSB/MSB-based Asymmetric FFE | 3-tap LSB/MSB-based Asymmetric FFE | 2-tap FFE + CTLE + Pre-emphasis
Nonlinearity compensation | Full | Full | Partial | Partial | Full
Method type | Digital | Digital | Analog | Analog | Analog
测试指标（经第三方检测报告认定）与国内外领先技术对比
技术指标名称 | 任务书指标 | 实测指标 | 是否满足
速率 | ≥ 56 Gbps | 56 Gb/s | 完成
功耗 | < 400 mW | 152 mW | 完成
测试指标（经第三方检测报告认定）与任务书指标对比

## Slide 12
PAM4 RX: signal equalization, decoding, and clock recovery
Two-stage CTLE to compensate signal in frequency domain
¼ rate architecture，3 comparators to adjust top, middle, and bottom eyes separately
Clock generated by DLL CDR, adopts jitter compensation to improve quality of output data

## Slide 13
PAM4 RX: signal equalization, decoding, and clock recovery
Implemented in 40nm CMOS technology，0.58 x 0.34 mm2 of core area
Error-free under 60-Gb/s with PRBS7/15, 70.8 mW of total power
Eye diagram of output MSB under ¼ rate
Eye diagram of output LSB under ¼ rate
Eye diagram of output clock under ¼ rate
Die photo
Bathtub curve
Power breakdown
12

## Slide 14
 | JSSC’19 | JSSC’19 | VLSI’14 | JSSC’17 | VLSI’14 | This work
Technology | 28-nm | 40-nm | 65-nm | 65-nm | 28nm | 40-nm
Architecture | 1/4-Rate NRZ | 1/4-rate NRZ | 1/4-rate NRZ | 1/4-rate NRZ Adaptive LPF BW in CDR | 1/4-rate NRZ Split path CDR | 1/4-rate PAM4, JCCDR
JTOL [UIPP] @ 3dB bandwidth | None @ 1 MHz | 0.22 UIPP** @ 4 MHz | 0.1 UIPP @ 1 MHz | 0.41 UIPP @ 20 MHz | 0.2 UIPP @ 8 MHz | 0.2 UIPP 40 MHz
JTRAN [dB] @ 3dB bandwidth | None | 0 ~ -3 dB @DC ~ 4 MHz | 0 ~ -3 dB @DC ~ 1 MHz | 0 ~ -3 dB @DC ~ 4 MHz | 0 ~ -3 dB @DC ~ 3MHz | <-8 dB @All band
Data rate [Gb/s] | 2-pairs × 16 | 25 | 14 | 40 | 4-lanes × 40 | 60
Power [mW] | 2-pairs × 16.06 | 27*** | 7.8 | 225 | 4-lanes × 175 | 70.8
Power efficiency [pJ/bit] | 1.004* | 1.08*** | 0.56 | 5.625 | 4.375 | 1.18
Supply voltage (V) | 0.9 | None | 0.8 | 1.2 | None | 1.0
测试指标（经第三方检测报告认定）与国内外领先技术对比
技术指标名称 | 任务书指标 | 实测指标 | 是否满足
速率 | ≥ 56 Gbps | 60 Gb/s | 超额完成
功耗 | < 400 mW | 70.8 mW | 超额完成
测试指标（经第三方检测报告认定）与任务书指标对比

## Slide 15
VCSEL TRX Demo：56-Gb/s PAM-4 VCSEL TX and RX
PAM4收发机芯片演示视频 ESSCIRC 2023+VLSI2021 Fuzhan Li_哔哩哔哩_bilibili
Link
QR code

## Slide 16
CMOS mmWave Phased-Array IC

## Slide 17
Starlink Ground Dish
Starlink Satcom
Mechanical satellite tracking employed
Utilization of electrical and digital beamforming
Architecture designed to minimize beamforming IC usage
Focus on combining individual PAs and LNAs for gain enhancement

## Slide 18: A Ka-Band Phased-Array Tx SoC in 40nm CMOS

## Slide 19: Area Efficiency Comparison
JSSC 2022, W band
2 x 2 mm2
w/o LO Gen.
This work, 28 GHz
1.87 x 1.16 mm2
with LO Gen
JSSC 2010, 60 GHz
2.9 x 1.4 mm2
w/o LO Gen.
TMTT 2021, 38 GHz
4.3 x 2.2 mm2
w/o LO Gen.

## Slide 20
Phase Shift and Gain Control Demo
  Orthogonal phase shift and gain control

## Slide 21
Beamsteering Demo

## Slide 22: Ka-Band Cascaded QPLL

## Slide 23: 28GHz Dual-Loop PLL Architecture

## Slide 24
Experimental Results
The 1st-stage RF SSPLL dominates the overall jitter
  1st-stage contributes 54.4-fs out of 56.8-fs total rms jitter
  High frequency VCO phase noise is sufficiently attenuated
  Over 1 kHz to 100 MHz range, QVCO PN profile is well above QPLL

## Slide 25: Performance Comparison
 | Hu ISSCC20 | EK JSSC18 | Yang ISSCC22 | Du VLSI21 | Kim JSSC19 | Liao JSSC20 | This work
Tech | 28nm | 28nm | 7nm | 28nm | 65nm | 45nm | 40nm
Arch. | CS + Harmonic extraction | Single-stage | Harmonic mixing | Harmonic extraction | Cascaded SS+QILO | Cascaded RSPLL+ ILFM | Cascaded SS+DP-SS
Freq. (GHz) | 21.71~ 26.49 | 23.3~ 30.2 | 25~28 | 24~31 | 28~31 | 33.6~36 | 24.0~ 29.8
Freq. range | 19.3% | 25.8% | 11.3% | 25% | 10.1% | 6.9% | 21.4%
Ref. (MHz) | 250 | 491.5 | 74 | 50 | 100 | 80 | 250
Jitter (fs) | 75.89 (10k~30M) | 114 | 88 | 199 (10k~30M) | 76 (1k~30M) | 251 (10k~10M) | 56.8 (1k~30M)
Spur (dB) | -45 | -65.1 | -61 | -65 | -58 | -60 | -55.6
Pdc (mW) | 16.5 | 31 | 12.9 | 11.5 | 41.8 | 20.6 | 42. 1
FoMjitter (dB) | -250.2 | -244 | -250 | -243.3 | -246.1 | -238.9 | -248.6
FoMjitter-N (dB) | -270.4 | -261.2 | -275.8 | -270.9 | -270.7 | -265.3 | -269.1
Area | 0.5 | N. M. | 0.24 | 0.3 | 0.32 | 0.41 | 0.4

## Slide 26
High-SPLIQ IC Needed for the New Era

## Slide 27
J. Albrecht et al., IEEE CSICS (2010).
I. C. Kizilyalli et al., “Wide band-gap semiconductor based power electronics for energy efficiency” (ARPA-E, Washington DC, 2018)
GaN for mmWave
GaN for power management
K. Shinohara, “III-Nitride millimeter wave transistors”, Chapter 4 in III-Nitride Electronic Devices, Elsevier (2019).
2025/10/22
26
High-Speed High-Power
High5 Semiconductor Ltd. Proprietary and Confidential. Protected under NDA. Copyright 2024.
Charger and power supply
0.01

## Slide 28
https://github.com/HKUST-ECE-IC-Design-Center-OWL/ISEE-Complex-Signal-Co-simulation-Platform-For-Intergrated-Circuit-and-System-Design
QAM-64 constellation with low EVM
QAM-64 constellation with high EVM (bad linearity)
Large signal performance of a mmWave power amplifier (PA),
including Pout, Gain and PAE
High-Linearity
ACPR from ISEE
(Integrated System Engineering Evaluator),
a simulation platform developed by OWL)

## Slide 29
System-in-Package
GaN PA
DC-DC
SOI LNA
CMOS TRx
Controller
RF Switch
Compact Package
Designed to achieve highest-level of integration in a small form-factor and includes multiple functions IC with multiple processes
This RFFE SiP includes 56 SMDs, 9 Acoustic filters, 4 HBT PAs, 2 SOI Switches, 1 SOI LNA, and 1 CMOS controller
High power dissipation device like DC-DC converter and GaN PA in the same package
Multiple-tech chips in a single package
High-Voltage High-Power Buck Boost Converter
EPC 140W Micro SmartPower
Type-C Bidirectional PD3.1/Max 140W
Type-A multi-channel fast charging
Intelligent power allocation for multi-port high-power charging
Built-in dual DC-DC
Supports 2C1A independent fast charging
Supports dual PD3.1 simultaneous charging and discharging
Solar energy charging
28V-5A discharge; 28V-2A charge
Multiple over-voltage, over-current, and over-temperature protection
High-Integration

## Slide 30
Trade-off between Q factor, inductance density, and power handling capability
Directly using PDK inductor
  L = 138 pH
  Q = 33
Custom-design optimized inductor
  L = 153 pH
  Q = 47 (42% higher)
High-Quality Factor Passives

## Slide 31
New Potential Applications in the 6G Era

## Slide 32: New Opportunities: Optical-Wireless Hybrid Link
Fiber-Wireless Hybrid Network: Cascaded Topology
Evolution of Cellular Networks
[2] X. Pang, JLT 2014
Fiber-Wireless Network
5G mobile network requires ultra-dense cellular cells
Backhaul links deployment is challenging
Fiber-wireless networks provide high performance and flexible backhaul link connections

## Slide 33: New Opportunities: Optical-Wireless Hybrid Link
Fiber-Wireless Hybrid Network: Parallel Topology
Under good weather condition: mmWave + Optical in parallel
Under bad weather condition: mmWave only

## Slide 34: Optical-Wireless Hybrid Link for SatCom
AOCS: Attitude and Orbit Control System
OCT: Optical Communication Terminals
[Okada. Tokyo Tech]
Mixed usage of OWC and mmWave links for LEO SatCom
  Optical: communication between satellites
  mmWave: between satellite and ground base station

## Slide 35: Optical-Wireless Hybrid Transceiver Architecture
Optical-In-mmWave-Out + mmWave-In-Optical-Out

## Slide 36
6G Technologies & IC Design
Research @ HKUST

## Slide 37
An Area of Excellence Project (AoE/E-601/22-R)
Started Jan. 2023 and Supported by the Hong Kong Research Grant Council
Coordinating
University:
6G: Wireless Access and Connectivity for an Intelligent and Sustainable World

## Slide 38
The AoE Team
K. HUANG
Jun ZHANG
Song GUO
C. Y. TSUI
R. MURCH
K. B. LETAIEF
Qian ZHANG
V. N. LAU
A. ZHANG
Jiaya JIA
Communication
/ Signal
Processing
Networking
Electromagnetics / Antennas / IC Design
AI / Machine
Learning
Multidisciplinary Team with Complementary Strengths
Patrick YUE

## Slide 39
Optical Wireless Lab (OWL🦉) Chip Gallery

## Slide 40
港科大光电无线实验室个人主页-哔哩哔哩视频 (bilibili.com)

## Slide 41
谢谢!
Thank you!